## Slide 1: Reservoir Analysis for Deep Direct-Use Feasibility Study in East Texas
Joseph Batir, Maria Richards, and Harrison Schumann
Southern Methodist University Geothermal Laboratory
Jbatir@gmail.com
GRC Technical Talk, Monday October 15, 2018

## Slide 2: Research Problems
A low temperature geothermal resource exists in the Texas/Louisiana Gulf Coast, most suitable for direct-use applications. How do we turn a low-grade heat resource into a high value economic product?
Can a turbine air inlet cooling system using the geothermal resource - through the application of an absorption chiller –increase the efficiency of the gas turbine system and do so economically?
Outline
Geologic Overview
Reservoir Properties Review
NGDS Data Review
New data
Results and Conclusions

## Slide 3: Research Questions
What is the temperature and volume of the low-temperature geothermal resource in the vicinity of the Eastman Chemical Power Plant near Longview, Texas?
Is this an economically feasible geothermal resource for turbine air inlet cooling?
Analysis Methods
Literature review of previous work in the area
Examine National Geothermal Data System (NGDS) for thermal regime, regional tectonics, and reservoir properties
Examine Railroad Commision of Texas (RRC) data to supplement reservoir properties, reservoir production, and formation depths

## Slide 4: Application: Turbine Inlet Cooling (TIC)
Well location and depth
Formation temperature
Pipeline lengths
Tank volume
Chiller capacity
Chilled water dispatch to compressor inlet
Power market
Optimization variables:
Craig Turchi et al., Wednesday 2:40- 3:00 Industrial Uses

## Slide 5: Study Area
Eastman Chemical Company
  Southeast of Longview, Texas
  Own mineral rights in plant area
  235 MW Gas-turbine power plant
10 km radius circle – primary focus
20 km radius circle – geologic correlation

## Slide 6: Regional Geology
East Texas
Western flank of the Sabine Uplift
Eastern flank of the East Texas salt basin
(modified after Hammes et al., 2011)

## Slide 7: Area Tectonics
No major faults, growth fault to north
Salt Pillows to the west and north
Sabine Uplift to east
(Tectonic data from Ewing, 2001)

## Slide 8: Stratigraphic Section
Primary target – Travis Peak Formation
Secondary targets – Cotton Valley (deeper); Pettett (shallower)
Study area is Shoreface to shallow marine
Reservoir quality can vary significantly
(modified after Hammes et al., 2011)
primary target
secondary target

## Slide 9: Reservoir Hydraulic Properties
Field-scale published data sources for the parameters:
Average/Maximum/Minimum of
    Porosity
    Permeability
    Reservoir thickness

## Slide 10: Well data
Texas RRC Public Data
  Downloaded from Drillinginfo.com
1000's of wells available
  Formation depth - used to calculate Formation thickness
  Production/Injection interval
  Production/Injection history
  Well logs (.TIFF) for most wells

## Slide 11: National Geothermal Data System
121 BHT derived heat flow from SMU node
  Can increase heat flow resolution using available .TIFF well logs
No additional tectonic information
No additional reservoir properties information
Production and Injection data available – still to be incorporated

## Slide 12: New Data

## Slide 13: Thermal Data
121 original BHT derived heat flow sites
Now > 1400 sites within the 20 km radius
  Pitman and Rowan (2012) thermal conductivity estimates used in heat flow calculation
  Increased resolution
  Improved total thermal heat in the reservoir

## Slide 14: Results

## Slide 15: Regional Tectonics impact on thermal regime
No significant change in
  Gradients
  Formation tops

## Slide 16: New Surface Heat Flow
Mineral Rights area consistent
Increased variability in 20 km

## Slide 17: Reservoir Properties
* RFC = Reservoir Flow Capacity
**RPI = Reservoir Productivity Index, a value below 10 would require hydraulic stimulation
+ Thickness is an average based on the difference between formation tops/bottoms (MAX) and injection perforations (AVE) and hydrocarbon productivity zones (MIN).

## Slide 18: Thermal Properties
Minimum target formation temperature is 100 °C
Geologic Unit Name | 20 km Median Top (m) | 20 km Median Bottom (m) | Median Thickness (m) | Median Top Temperature (°C) | Median Bottom Temperature (°C) | Temperature Standard Dev. (°C) | Median Formation Gradient (°C/km)
Pettit Limestone | 2245 | 2319 | 74 | 99 | 101 | 7 | 27
Travis Peak Sandstone | 2319 | 2881 | 562 | 101 | 120 | 7 | 33.8
Cotton Valley Sandstone | 2881 | 3354 | 473 | 120 | 134 | 10 | 29.6

## Slide 19: Travis Peak Formation Top depth (2,000 m to 2,400 m) Well sites (green dots)

## Slide 20: Travis Peak Formation Thickness
Consistent thickness under Mineral Rights
Thickness greater in 10 km radius to south and east

## Slide 21: Travis Peak Heat Density
Mineral Rights area - average
SE and NW areas variable

## Slide 22: Conclusions
Significant amounts of data are publicly available for geothermal reservoir analysis
  National Geothermal Data System (NGDS), previous publications, and state organizations
  Data are more easily accessible through proprietary data aggregation companies like Drillinginfo and IHS Energy
In East Texas, the Travis Peak Formation is a promising geothermal reservoir for direct use applications
  The reservoir heat density varies from ~150 - 300 MJ/m3, which would have a significant impact on economic potential of the reservoir
  NREL is working on economically viability of reservoir (See Craig Turchi talk on Wednesday afternoon)
    Concerns - high salinity in the Texas formation fluids (~200,000 TDS)
    Concerns - drilling cost for two production wells
Results presented here are applicable to several gas turbine power plant operators within our study area
  The workflow and analysis methodology can be utilized in other prominent hydrocarbon producing basins to discover other deep direct use geothermal reservoirs

## Slide 23: Thank you!
Sharon Fields and Cathy Chickering Pace of the SMU Geothermal Lab
Drillinginfo, ESRI, and IHS for educational software licenses
XTO Energy donated .LAS well logs
Collaborators: National Renewable Energy Lab (NREL) Eastman Chemical Company Turbine Air Systems (TAS)
This work was authored in part by the National Renewable Energy Laboratory, operated by Alliance for Sustainable Energy, LLC, for the U.S. Department of Energy (DOE) under Contract No. DE-AC36-08GO28308. Funding provided by U.S. Department of Energy Office of Energy Efficiency and Renewable Energy Geothermal Technologies Office under Contract No. DE-EE0001514. The views expressed in the article do not necessarily represent the views of the DOE or the U.S. Government. The U.S. Government retains and the publisher, by accepting the article for publication, acknowledges that the U.S. Government retains a nonexclusive, paid-up, irrevocable, worldwide license to publish or reproduce the published form of this work, or allow others to do so, for U.S. Government purposes.