## Slide 1
Trenton T. Cladouhos, Susan Petty, Michael W. Swyer, Matthew E. Uddenberg, and Yini Nordin
2014 Results from Newberry Volcano EGS Demonstration
Stanford Geothermal Workshop
January 27, 2015

## Slide 2: Newberry Volcano EGS Demonstration
Geothermal well drilled in 2008
55-29
10,060 feet, 3067 m deep
620⁰F, 330⁰C
No hydrothermal system
DOE ARRA grant awarded in 2009
Three phases
50% cost share
DOE funding ends Sept 2015
Notes: 20 km away ~7 km across Caldera, 4000 ft of relief, Paulina Peak just under 8000 ft, Pre-caldera peak may have been 10,000 ft

## Slide 3: AltaRock TZIM Technology
Challenge: Low flow per EGS well Need >75 l/s, >1200 gpm
Solution: Multiple zone stimulation through thermally-degradable zonal isolation materials (TZIM)
Non-mechanical zonal isolation
No rig required during treatment
Non-hazardous breakdown products
A suite of materials developed that degrade with time and temperature
  Lab tested from 74C-315  C
Notes: I added the diverter degradation results from Daniel’s Stanford paper. The key here is to show that we have a variety of materials that will degrade at different temperatures. Every stimulation we design will be unique and targeted to fit the characteristic of the reservoir.

## Slide 4
Multizone Stimulation and TZIMs
Stage 1
Cold Water
Heat-up and flow back
Stage 2&3
Cold Water & TZIM
Hot Water

## Slide 5
Mapping Newberry EGS with Microseismic Array
  15-station seismic array (installed 2012)
  8 borehole (250 m deep) geophones
  7 surface geophones
  Real-time telemetry
  Strong motion sensor in nearest building (ISMP)
2 Hz, 3 component
geophones
1 km

## Slide 6: Rig Operations 2014
New Liner
9 5/8” tie-back
2012 stimulation problems
Leaks in 13 3/8” casing at 1800ft (PAS) and 2250ft
Blockage in open hole at 6888ft
2014 Repairs
Installed 9 5/8” tieback
Installed perforated liner

## Slide 7: Electric Centrifugal Stimulation Pumps

## Slide 8
Wellhead pressure and flow rate during stimulation
Round 2 (Nov 11-20)
Round 1 (Sept 23- Oct 15)
heat up /fall-off
heat up / fall-off
srt
Max WHP stim
TZIM
TZIM &
tracer
srt
srt
srt
srt
srt
f&I PTS
flow back
flow back
inj PTS
Max WHP
stim
srt = step-rate test
14 days
8 stim days
8 stim days

## Slide 9: Stimulation Start
Stimulation initiated
(aseismic)

## Slide 10: Injectivity Index
initial
final
Max WHP

## Slide 11: Pressure Fall-off Test
Pre-stim permeability (modeled) | 0.01 md 10-17 m2
Fall-off analysis permeability* | 1.46 md (10-15 m2)
Skin factor | -6.19
Injection shut-off on 10/15/14.
Pressure fall off monitored down hole for 12 hours.
Data analyzed with Horner plot.
Transmissivity calculated to be (957 md-ft).
*Assuming 200m reservoir height as presented in Cladouhos et al. 2011

## Slide 12: Seismicity Rate

## Slide 13
400 Micro-Seismic Event Locations (hand-picked)
1 km
Map View North View

## Slide 14: Micro-Seismic event size distribution
Mw 2.3
Mw 0.0
b-value 1.01
Log (N)

## Slide 15: Flowing Temperature Survey, October 15
8393-8415
8791-8835
9320-9500
6878-6929
8200-8240
8145
7477
Logged on 10/15 with outflow rate of ~100 gpm (6.3 l/s)

## Slide 16: Progression of seismicity from well
MD potential exit depths
6863’
8390’
9624’
9950’
8800’
error bars

## Slide 17: PTS Logging to document TZIM effect

## Slide 18
Evidence for TZIM Blocking

## Slide 19: Nov. 24-25 flowback: TZIM degradation product
Partial degradation
AltaVert 251 degrades
at >200 C / 400 F
Fully in less than a week
Results from Peter Rose, EGI

## Slide 20: Nov. 24-25 flowback: Tracer Returns
1,3,6 NTS
Injected prior to granular TZIM
206,000 gallons inject after
9.1% mass recovered
2,7 NDS
Injected prior to fiber TZIM
153,000 gallons injected after
18.1% mass recovered
116,000
gallons
flowed
Tracer return model pending
Results from Peter Rose, EGI

## Slide 21: Potential Production Well Targets
Work in Progress
Based on 100 best-located seismic events
Production well will be stimulated (single and dual)
cased
open
Results from Foulger Consulting

## Slide 23
200 m
300 m
Under
Over
200 m
15°
20°
8°

## Slide 24: 55A-29 Well Target Options
South-side, Deep
PROS
  Targets depths with most flow in 55-29
  Targets hottest rock
  Targets Deep MEQs
  Simpler well course
CONS
  Does not target majority of 2014 MEQs
  Deeper = higher drilling cost
North-side, Shallow
PROS
  Targets volume with most 2014 MEQs
  Targets Deep Shallow MEQs
CONS
  Requires S-curve drill path
  Targets cooler rock
  Stim. of 55A will likely grow up (?)

## Slide 25
Thanks!
Follow us!
blog.newberrygeothermal.org
Facebook - NewberryEGS
This material is based upon work supported by the Department of Energy under Award Number DE-EE0002777.
Disclaimer: This report was prepared as an account of work sponsored by an agency of the United States Government. Neither the United States Government nor any agency thereof, nor any of their employees, makes any warranty, express or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States Government or any agency thereof. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States Government or any agency thereof.

## Slide 26
Acknowledgement
Funded by the DOE via Recovery Act DE-EE0002777/004

## Slide 27
Micro-
crystalline
Granodiorite
Microcrystalline Granodiorite
Chlorite alteration of mafics
Subvolcanic Basalt
Epidote veinlets, metasomatic alteration
Subvolcanic Basalt
Geology of 9500ft flow zone

## Slide 28
cased
open
Depth (m)
2000
2200
2400
2800
3000
3200
Potential Production Well targets
Cross-section looking west
P&T axes from moment tensor solutions
0
-200
200
South - North (m)
2600

## Slide 29: All P&T Axes
Axis Trend Plunge
1. σ3 012.2 57.4
2. σ2 152.8 26.3
3. σ1 252.0 17.9
T-axes from BHTV breakouts
P-axis if strike-slip regime
P-axis if normal regime

## Slide 31
300 m
Map View
Best MEQ locations (N=100)
Injection well
Production well
Injection well
Production
well
2015: Plan, Drill and Stimulate Production Well
West view cross section
Best MEQ locations (N=100)

## Slide 33
Mo = G Vinj
RMA
RatonB
Prague, OK
Basel
M 2
M 4
M 3
M 5
10,000 m3
63,000 bbl
2.6 mgallons
8.1 acre-ft
Soultz
Injected Volume vs. Earthquake Magnitude
(McGarr 2014)

## Slide 34
Oregon LiDAR Consortium: Deschutes and Newberry, summer 2010
Vents and
Fissures
Ring
Fractures
Scarps
Extension Direction (consistent with
Regional focal mechanism inversions)
E-W Shmin

## Slide 35
Set 1
Set 2

## Slide 37
Borehole Televiewer Log: Newberry Well 55-29
Measured Depth, ft
2-Way Travel Time Amplitude
Fast Slow Low High
N E S W N
N E S W N
N E S W N
N E S W N
2-Way Travel Time Amplitude
Fast Slow Low High
L
F
B
B
F

## Slide 38: Stress Model
Profiles of Stress Magnitudes
Stress Orientations from BHTV
density logs
injection test
BH breakouts
rock strength

## Slide 39: Innovation: Centrifugal Stimulation pumps
Challenge: Stimulation pump reliability, suitability, and high rental cost
Solution: Centrifugal, electric pumps
Two 14 stage centrifugal pumps connected by 10 inch pipes & four valves
HP (Newberry) Mode: in series with bypass line to allow sufficient flow to keep pumps cool when injecting to very low permeability wells
LP Mode: in parallel for 1450 psi (100 bar) and 1600 gpm (100 l/s)
2850 psi – 195 bar
800 gpm – 50 l/s
Pump curves for HP Mode